## Slide 1: Project Occupancy Control System
Final Demo – group 2

## Slide 2: Delivery
Wireless mesh network using ESP32 nodes
“Gate” subsystem using C++ on the ESP32 boards
Gate display simulation on a C# application
“Gate” subsystem simulation using C on arduino
“Toilet” subsystem simulation using C on arduino
Control Panel C# application
Project Documentation
CO2 measuring and max occupancy algorithm

## Slide 3: Wireless mesh network
We made a wireless mesh network on the ESP32 boards to communicate between all gates and the control panel. This makes the system independent and decentralized, thus ensuring proper functioning of all nodes, should any of the others fail

## Slide 4: “Gate” subsystem
We made a “Gate” system on the ESP32 boards connected in the mesh network. It consists of:
2 ultrasonic sensors detecting direction
1 servo motor simulating an electronic door/gate
1 ultrasonic sensor detecting queue in front of the gate
Connection with a C# application simulating a display in front of the gate to display information to visitors
Help button to request assistance or signal emergency

## Slide 5: Control Panel Application
We made a C# application connected with serial communication to a ESP32 board, that is in the wireless mesh network. It displays all the important information of the building – occupancy, help requests, gate status, CO2, etc.

## Slide 6: Gate and toilet simulation
Due to restricted ammount of hardware, we were forced to create simulation devices that would not use ultrasonic sensors or ESP32 boards and include them in the control panel application to create a more realistic environment. A simple CO2 node is included to send data to the control panel

## Slide 7: What went wrong
network functionality in final demo
Commands from control panel
Group communication

## Slide 8: Reccomendations
Better time management and testing
1
Improve control panel by enabling it to lock gates manually (by building administrator/security officer)
2
Replace ESP32 boards with better hardware
3

## Slide 9: Questions?